Note:	TIRIOCFG

Product:	TI Remote I/O Setup

Date:	2/26/99

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Setup and Configuration of the TI Remote I/O Card

- Check to see if there is an open ISA slot in the unit.

- Configure the card via the jumper setting that are located on the Remote I/O card for:

Base Address= D000

Card Interrupt= 5

*Note:  If you already have a card in the unit that is using the same Base Address and Interrupt as listed above, change the other card’s Address and Interrupt.

- Check the diagram below to setup the Interrupt for the TI Remote I/O card.

- In Interact open the property sheet for the TI Remote I/O Driver (TIRIO) and set the Base Address and Interrupt to match the cards jumper settings.

5)	Configure the rest of the driver, Acquisition Blocks and Write Buffering, the way you want it.