Note:	IMD_Appnote

Product:	IMD and NBIOS

Date:	9/16/99

# Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Setup of the Interact Modem Driver with Lantastic Z and the NBIOS Driver.

Note:  It is recommended that the setup of this application be performed with both modems in the place of testing.  This will keep the trouble-shooting to a minimum.

Parts needed for this setup:

- Two 100% Hayes compatible modems (from the same manufaturer is recommended.)

- Lantastic Z Software

- Interact Development

- Two powerstations or PC’s

- LANTASTIC Z INSTALL

- Install Lanstatic Z on your PC.

- Copy the MPORT and AILANBIO to the Powerstation in the NET directory.

- Edit the NET.BAT file.  Use these lines only.

LH  MPORT  PORT=(the port the modem is connected to)  BAUD=19200 IRQ=(4 or 3)

LH  AILANBIO  ADAPTER=0

- EDIT THE AUTOEXEC.BAT ON THE POWERSTATION

- Remove the REM statement from the line that calls the NET.BAT.

- Add the REM statement to the lins that call the PSU.

- Add a line that calls the AM.EXE in the Interact\Am directory.

- EDIT THE NBIOS.FIL FILE ON THE PC

- Go to the Interact\Drivers\Nbios directory on the PC.

- Edit the NBIOS.FIL file.

- The file should look like this:

8

NBIOS.EXP

NBIOS.TXT

NBIOS.HLP

NBIOS.ERR

NBIOS.ICN

NBIOSR.EXP

NBIOSR.TXT

NBIOS.FIL

8

NBIOS.EXP

NBIOS.TXT

NBIOS.HLP

NBIOS.ERR

NBIOS.ICN

NBIOSR.EXP

NBIOSR.TXT

NBIOS.FIL

NBIOS   300  11

NBIOS   400  12

- ADD THE NBIOS AND IMD DRIVER TO THE APPLICATION

- Add the Nbios driver and the Interact Modem driver to the application.

- CONFIGURE THE NBIOS DRIVER

- Set the Node Name for the Powerstation.

- Leave the Lan Adapter Number at 0.

- The rest of the configuration of the Nbios driver can be left at its defaults.

- CONFIGURE THE IMD DRIVER

- Set the Operation Mode to Network Link.

- Set the Port Number to the Com Port that the Modem is connected to.

- The Modem Comands are up to the customer to setup, they depend on the manufacturer of the modem.

NOTES:

- Error Checking and Data Compression must be turned off in the modem.

- Asyncronous Mode must be turned on.

- The modem must be forced to the Baud rate that was set with the MPORT.

- The Phone List, Connections, and Triggers are up to the type of networking that the customer will be doing.  For additional information on these settings, check the On-line Help.