Note:	Floppy Drive Connection

Product:	P3, P5 Flash Units

Date:	12/11/95

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

The PowerStation Supports a parallel floppy disk drive that can ONLY be used for backing up or logging INTERACT data log files (I.E. those files located in the application’s LOG directory).  This drive will be recognized by the PowerStation as drive C.

Computer Technology Corporation recommends using the PacRim model P1.2 (5 1/4 in.) floppy disk drive or the P3.5 (3 1/2 in.) floppy disk drive.

To use this drive with the PowerStation you must copy the PRSPF.SYS file from the disk drive installation disk into an Interact Project Manager (IPM) STARTUP subdirectory.  This sheet assumes you are using a PacRim model P1.2 or P3.5 disk drive and provides information on installing the PRSPF.SYS file.  However, this process would be similar if using any other parallel floppy disk drive.

You must be familiar with downloading projects to the PowerStation prior to following these steps (if not, see appnote on Creating a Project).  Downloading projects is also described in the PowerStation documentation.

1.	Install the disk drive following the documentation provided with the drive.

2.	Use a computer with the Interact Project Manager (IPM) installed.  This disk comes with the PowerStation.

3.	Connect the serial download cable between the computer and the PowerStation.

4.	Go to the directory on the computer where you installed IPM.  The default directory would be:

C:\INTERACT\PS

5.	Go to the projects subdirectory:

C:\INTERACT\PS\PROJECTS

6.	Go to the specific project you will be using with this disk drive:

C:\INTERACT\PS\PROJECTS\project_name

7.	Go to the STARTUP subdirectory of the project:

C:\INTERACT\PS\PROJECTS\project_name\STARTUP

8.	Insert the PacRim installation disk into the computer.

9.	Copy PRSPF.SYS from the installation disk into the project’s STARTUP directory on the computer.

10.	Add the following line to the CONFIG.SYS file located in this STARTUP directory.  If a CONFIG.SYS file does 	not exist, create one in this directory.

DEVICE=B:\PRSPF.SYS /P /T1=5H 	for 5 1/4 in. drive

or	DEVICE=B:\PRSPF.SYS /P /T1=3H 	for 3 1/2 in. drive

where:  	/P1 indicates LPT1

/T1=5H indicates a 5 1/4 in. high density drive

/T1=3H indicates a 3 1/2 in. high density drive

11.	Download the project to the PowerStation following the procedures listed in the PowerStation documentation (or 	the appnote on downloading a project).

12.	This drive will now appear as drive C for INTERACT logging and backup purposes.

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.   w   Milford, OH  45150
Phone (513) 831-5042   w   Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com   w   E-Mail:  support@ctcusa.com