Note:	Installation of the Network Adapter and Software

Product:	P3 and P5 PowerStation

Date:	12/10/95

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

This example is using Artisoft Lantastic Network and Artisoft NODERUNNER or compatible adapter card.

1.	Select IRQ# and I/O base address for the Network adapter card.

Example:	IRQ#5

I/O Base address 300

Install Network Adapter Card in PowerStation.

2.	Using Interact Project Manager (IPM) create a project to be downloaded to the PowerStation.

3.	At the DOS prompt go to the STARTUP directory of the project:

CD C:\INTERACT\PS\PROJECTS\project_name\STARTUP

From Lantastic Drivers Disk copy the following files to the STARTUP subdirectory:

NODERUN.EXE - Noderunner Network adapter driver

AILANBIO.EXE - Lantastic NetBios Emulator

4.	Using DOS EDIT or other text editor, create an AUTOEXEC.BAT file in the STARTUP subdirectory.

Type the following lines:

B:\NODERUN

B:\AILANBIO

Note: - B: is the PowerStation drive where Interact will be installed.

5.	Transfer the project to the PowerStation;  after the unit reboots, the Network files will be executed.

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.   w   Milford, OH  45150
Phone (513) 831-5042   w   Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com   w   E-Mail:  support@ctcusa.com