Note:	NT DOS Client Networking

Product:	P1-P7 Powerstations

Date:  4/13/00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Setup and configuration of DOS level network printing on an NT Server Network for both TCP/IP and NetBEUI

NOTE: This application note is not intended for Powerstations running the Machine Shop Shell or Machine Logic.  It is the end user’s responsibility to obtain and properly install the software required to complete this application note.  The presence and input of the Network Administrator is critical to the completion of this Application Note.

Items needed:

Two formatted disks

Powerstation P3 thru P7

Powerstation MUST have MS-DOS 6.22 installed.

# Creating the MS-DOS Client Disks

- You will need to make the DOS Client Disk from the NT Server.

- On the server go to the START button, then to PROGRAMS.

- Choose Administration Tools.

- Choose Network Client Administrator.

- Select Create Network Install Disks.

- Put a floppy disk in drive A:

- Follow the instructions.

# Installing the DOS Client on the Powerstation

- Insert disk #1 in the floppy drive of the Powerstation.

- Type in A: and hit the ENTER key.

- At the A:\> prompt type in SETUP and press the ENTER key.

- At the initial setup screen, press the ENTER key.

- When prompted for a directory leave at the default C:\NET and hit the ENTER key.

- The Setup will ask for a network interface card, select the NE2000 Compatible and press the ENTER key.

- Press the ENTER key again.

- The Setup will ask for an “Username” to be used for networking.  Use the Username that the Network Administrator has given to you and press the ENTER key.  NOTE: If you do not have a username at this time, do not proceed with the rest of the application note until you contacted your Network Administrator.

- Select Change Setup Options:

- Change the Redir Options to “Use the Full Redirector.”

- Change Startup Options to “Run Network Client.”

- Change Logon Validation to “Logon to Domain.”  ** Only if you are using Domains.

- Highlight “Listed Options are Correct” and press the ENTER key.

- Select Change Network Configuration:

- Select “Change Settings” and hit the ENTER key.

- INTERRUPT=10

- IOBASE=280

- Highlight “Listed Option are Correct” and hit the ENTER key.

- Press the Tab key to move the focus to the upper window.  Highlight NWLink IPX Compatible Transport.  Press the Tab key again to return the focus to the lower window and highlight “REMOVE.”  Hit the ENTER key.

- Select “Microsoft TCP/IP” by highlighting it and press the ENTER key.

- Highlight “Add Protocol” and press the ENTER key.

- Highlight “Microsoft NetBEUI” and press the ENTER key.

- Hit the Tab key to move the focus to the upper window.  Highlight “Microsoft TCP/IP.”  Press the Tab key again to return the focus to the lower window.  Highlight “Change Settings” and press the ENTER key.

NOTE:  If the server is using DHCP, then leave the settings at their default values.  If the server needs the Client to specify the IP and MASK addresses, contact your Network Administrator for the proper settings.

- Hit the Tab key to move the focus to the upper window.  Highlight “Microsoft NetBEUI.”  Press the Tab key again to return the focus to the lower window.  Highlight “Change Settings” and hit the ENTER key.

NOTE:  Contact your Network Administrator for the proper settings for these fields.

- Highlight “Network Configuration is Correct” and press the ENTER key.

- Select Change Names:

- If the Computer Name needs to be different than the Username, then change the computer name.  The Computer Name must be unique on the network.  If unsure, contact the Network Administrator.

- If using Worgroups, change the Workgroup Name to the appropriate Workgroup Name.  If unsure of this setting, contact your Network Administrator.

- If the server is using Domains, change the Domain Name to the appropriate Domain Name.  If unsure of this setting, contact your Network Administrator.

- Highlight “Listed Names are Correct”and press the ENTER key.

- Highlight “listed Option are Correct” and press the ENTER key.

- The Setup will prompt you for the “OEM Driver Disk,” insert Disk#2 and press the ENTER key.

- The Setup will prompt you for the “Microsoft Network Client for MS-DOS Disk,” insert Disk #1 and press the ENTER key.

- Setup will start the Installation Status screen.

- You will be prompted to remove any disks from the floppy drive, remove the floppy and press the ENTER key.

- The unit will reboot.

- At the C:\> prompt type EDIT  AUTOEXEC.BAT.  Modify the Autoexec.bat to look like the example below.

# Example Autoexec.bat

C:\NET\net initialize

@ECHO OFF

PROMPT $p$g

SET TEMP=C:\DOS

PATH C:\NET;C:\;C:\DOS;C:\CTC

REM ********************************************************************

REM Install Powerstation Special Functions

REM ********************************************************************

LH /L:1,5264 C:\CTC\BIOSTSR

REM ********************************************************************

REM Load VESA video support TSR if necessary

REM ********************************************************************

C:\CTC\ISVESA

IF ERRORLEVEL 1 GOTO NOVESA

GOTO YESVESA

:NOVESA

LH /L:1,5520 C:\CTC\VESA

:YESVESA

REM ********************************************************************

REM If an external mouse is connected, MOUSE will install successfully,

REM and NOMOUSE will do nothing.  If external mouse is not found, MOUSE

REM will fail, and NOMOUSE will successfully load.

REM ********************************************************************

C:\CTC\MOUSE

LH /L:1,56928 C:\CTC\NOMOUSE

REM ********************************************************************

REM Install TouchBase touchscreen drivers

REM ********************************************************************

SET TBDPATH=C:\TOUCH

SET TBDINT=61

LH /L:1,10016 C:\TOUCH\TBDRIVER /A:310 /I:15

LH /L:1,5936 C:\TOUCH\TBMOUSE 1

REM ********************************************************************

REM Set up Interact environment variables for CTC Shell

REM ********************************************************************

SET INTERACT=C:\INTERACT

SET INTERACT_FILES=C:\INTERACT\APPFILES

SET INTERACT_STARTUP=C:\STARTUP

REM ********************************************************************

REM Call AUTOEXEC.BAT file contained in project, if it exists

REM ********************************************************************

IF EXIST C:\STARTUP\AUTOEXEC.BAT CALL C:\STARTUP\AUTOEXEC.BAT

REM ********************************************************************

REM Uncomment next statements to load network batch file

REM ********************************************************************

REM CD \NET

REM CALL C:\NET\NET.BAT

REM ********************************************************************

REM Start the CTC Shell

REM ********************************************************************

CD \CTC

C:\NET\netbind.com

C:\NET\umb.com

C:\NET\tcptsr.exe

C:\NET\tinyrfc.exe

C:\NET\nmtsr.exe

C:\NET\emsbfr.exe

NET LOGON [USERNAME] [PASSWORD] /DOMAIN:[DOMAIN_NAME] /YES

NET USE LPT1: \\[SERVER_NAME]\[SHARED_PRINTER_NAME] /PERSISTENT:NO

CD CTC

PSU

NOTE:  The items in bold print are variables and should be replaced with the appropriate information for your network.