# MachineShop Download Quickstart Guide For Disk Transfers

This Quickstart Guide was designed by the CTC Training department to assist customers with MachineShop Download functions. While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

The MachineShop Toolbar

The Disk Transfer Connection is a transfer method that allows you to send projects to a removable Compact FLASH disk or network drive. This connection method allows Interact programs, applications and startup files to be easily copied to a runtime system.

Launching MachineShop and selecting a project to download:

- Start MachineShop by double-clicking the MachineShop desktop icon or choosing the Windows Start, Programs, MachineShop, MachineShop Toolbar.

- Choose the MachineShop ‘File’ menu.

- Choose ‘Open Project…’ and select the MachineShop project you want to download.

- Choose the ‘Open’ button. After selecting the project, the project name will be displayed in the upper right-hand corner of the toolbar.

MachineShop Toolbar

Part 1

Adding a connection:

If you have already configured a connection and have previously downloaded, go to Part 2.

Before transferring, you must define a Transfer Connection. This is how you will transfer files to or from the runtime system. The Transfer Wizard will allow you to quickly configure the connection.

To create a MachineShop connection with the Connection Wizard:

- Choose the Connection Wizard icon from the MachineShop toolbar. This is displayed to the left of the Transfer Connection Window.

Transfer Wizard icon and Transfer Window

- Choose the ‘Download to Runtime’ option on the Transfer Wizard. Download defines data that is being transferred to the PowerStation while Upload defines information coming from the PowerStation.

Transfer Wizard Step 1

- Choose ‘Next’.

- Choose ‘Define New Connection’. This will display the Add Connection Menu.

Defining a Connection Name

- Type a connection name. This will create a name for your connection so you may want to type a descriptive name such as “FLASH”.

- From the Connection type pull down menu, choose DISK. This will allow you to define a destination drive to transfer to.

- Choose ‘OK’.

- From the pull down, select the drive letter that contains the Compact FLASH disk. If you do not know the drive letter of your FLASH disk, open the Windows Explorer and explore the drives.

Notes:

The graphic on the left in the following menu is not a depiction of your PC. The pull down menu shown below is the map of your system. If you have not inserted your Compact FLASH into the drive, do so at this time and select the ‘< Back’ button on the menu. From the previous menu, choose ‘Next >’. This will allow the FLASH card insertion to be recognized.

Choosing FLASH Drive Letter

- Choose ‘Finish’.

Part 2

Sending your project:

If you do not have a connection in your pull down list named ‘FLASH’, go back to Part 1.

- Make sure the connection named ‘FLASH’ appears in the window as shown in the following menu.

Choosing a Connection

- Choose ‘Next >’.

- Depending on what you are transferring will determine how the following menu will be configured. (See below)

Selecting Transfer Options

If you want to overwrite the current project on the PowerStation or you are transferring to a PowerStation that does not contain a project, check the ‘Complete Project’ checkbox.

Note:

If you want to transfer specific components of a project you can uncheck the ‘Complete Project’ checkbox and choose any combination of the following:

Program Files – choose this option if you want to update or add an additional Interact module or driver to an existing project on the PowerStation.

Application Files – choose this option to transfer user created files. (Panels, alarm configuration files, etc.)

Startup Files – choose this option to transfer files that are located in the startup directory for your project.

For faster transfers, you may want to check ‘Updated Files Only’. This will send only files that have been modified since the last transfer.

4. Choose ‘Finish’. The files will now transfer to the Compact FLASH card.

Transfer Status Screen

- When the project has transferred, choose ‘Close’.

Warning To Laptop Users:

Always make sure that MachineShop has completed the project transfer before removing the FLASH disk. Removal of the FLASH disk during disk write operations can damage the FLASH card and cause unpredictable behavior. See the procedure below for information on proper PCMCIA FLASH disk removal.

PCMCIA FLASH Disk removal Procedures:

- From the Windows Desktop, double-click the ‘My Computer’ icon.

- From the My Computer Window, double-click the ‘Control Panel’ icon.

- Double-click the ‘PC Card (PCMCIA)’ icon.

- From the PC Card (PCMCIA) Properties menu, choose the Socket containing the FLASH Disk.

- Choose ‘Stop’. You will receive notification that it is safe to remove the FLASH disk.

- The FLASH disk can now be safely removed.

PC Card (PCMCIA) Screen