Note:	NT DOS Client Networking

Product:	P1-P7 Powerstations

Date:  	9/19/00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Setup and configuration of DOS level networking on an NT Server Network for both NWLink IPX and NetBEUI

NOTE: This application note is not intended for Powerstations running the Machine Shop Shell or Machine Logic.  It is the end user’s responsibility to obtain and properly install the software required to complete this application note.  The presence and input of the Network Administrator is critical to the completion of this Application Note.

Items needed:

Two formatted disks

Powerstation P3 thru P7

Powerstation MUST have MS-DOS 6.22 installed.

# Creating the MS-DOS Client Disks

- You will need to make the DOS Client Disk from the NT Server.

- On the server go to the START button, then to PROGRAMS.

- Choose Administration Tools.

- Choose Network Client Administrator.

- Select Create Network Install Disks.

- Put a floppy disk in drive A:

- Follow the instructions.

# Installing the DOS Client on the Powerstation

- Insert disk #1 in the floppy drive of the Powerstation.

- Type in A: and hit the ENTER key.

- At the A:\> prompt type in SETUP and press the ENTER key.

- At the initial setup screen, press the ENTER key.

- When prompted for a directory leave at the default C:\NET and hit the ENTER key.

- The Setup will ask for a network interface card, select the NE2000 Compatible and press the ENTER key.

- Press the ENTER key again.

- The Setup will ask for an “Username” to be used for networking.  Use the Username that the Network Administrator has given to you and press the ENTER key.  NOTE: If you do not have a username at this time, do not proceed with the rest of the application note until you contacted your Network Administrator.

- Select Change Setup Options:

- Change the Redir Options to “Use the Full Redirector.”

- Change Startup Options to “Run Network Client.”

- Highlight “Listed Options are Correct” and press the ENTER key.

- Select Change Network Configuration:

- Select “Change Settings” and hit the ENTER key.

- INTERRUPT=10

- IOBASE=280

- Highlight “Listed Option are Correct” and hit the ENTER key.

- Press the Tab key to move the focus to the upper window.  Highlight NWLink IPX Compatible Transport.  Press the Tab key again to return the focus to the lower window and highlight “CHANGE SETTINGS.”  Hit the ENTER key.

- Select “Ethernet_802.2” by highlighting it and press the ENTER key.

- Highlight “Ethernet_802.3” and press the ENTER key.

- Choose “Add Protocol” and press the ENTER key.

- Select Microsoft NetBEUI and hit the ENTER key.

- Highlight “The listed options are correct” and press the ENTER key.

- The Message “Setup will now configure the network drivers” will apprear.

- Remove the disk that is in the floppy drive and press the ENTER key, the unit will reboot.

- When the unit reboots it will ask if the User Name is what is displayed, hit the ENTER key.

- It will now ask for a password.  Password has to be eight characters or less.

- It will ask to confirm the password, type it in again.

- Exit the shell or Interact and then the Shell and get back to DOS.

- At the C:\CTC directory, type in CD\ and hit the ENTER key.

- Type in CD NET and hit the ENTER key.

- In the C:\NET directory type in NET and press the ENTER key.

- The Net Connections Dialog will appear.

- You are able to specify the path of the drive that you want to log to.

- You can browse the network for the drive by using the TAB key to highlight BROWSE.

  - In the BROWSE utility, you can find the drive on the network, if it is shared.

- Use the TAB key to highlight the “Reconnect at Logon” and press the SPACEBAR.

- Use the TAB key to select EXIT and press ENTER.

21.  When you reboot you will have the drive mapped.