Note: 	 PID and FPID functions

Product:  MachineLogic

Date:	   2/20/2001

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Introduction

This document contains information on the PID and FPID functions for MachineLogic.  The PID and FPID functions are available from the PCLC firmware library (*.fwl).

# PID

The parameters for the PID function are described below.

| Parameter | Data Type | Description |
| --- | --- | --- |
| ENABLE | BOOL | Enables the PID function |
| AUTO | BOOL | Selects between the Manual output or the calculated function output |
| PV | REAL | The actual value of the process being controlled |
| SP | REAL | The desired value of the process |
| XO | REAL | The manual output of the function |
| KP | REAL | The proportional constant (P) |
| TR | REAL | The integral constant (I) |
| TD | REAL | The derivative time constant (D) |
| CYCLE | TIME | Time between calls of the function block |
| XOUT | REAL | The output of the function (controlling variable) |

The PID inherently acts as a direct acting control loop.  However, if the negative of the integral value is used the controller will act in the opposite direction of the process value.

The value connected to CYCLE should correspond to or be less than the cycle time of the task where the function block is used.

FPID

The parameters for the FPID function are described below.

| Parameter | Data Type | Description |
| --- | --- | --- |
| REMOTE | BOOL | Selects between the remote and local set points (if True function uses SPR as the set point) |
| AUTO | BOOL | Selects between the manual and calculated output of the function |
| DIRECTN | BOOL | Switches the controller between a direct and reverse acting controller (if True then action is direct acting) |
| INTLCK | BOOL | Condition that will cause the function block to use the INTLCKV as the output |
| TSCAN | REAL | Time between calls of the function block |
| YMAN | REAL | Manual output of function |
| SPR | REAL | Remote set point of function |
| SPL | REAL | Local set point of function |
| X | REAL | The process value |
| KP | REAL | The proportional constant (P) |
| TI | REAL | The integral constant (I) |
| TD | REAL | The derivative time constant (D) |
| HIGH | REAL | Maximum Limit of Output |
| LOW | REAL | Minimum Limit of Output |
| INTLCKV | REAL | If INTLCK is True then function output will be set to INTLCKV value |

The FPID function can select between two different set points (Remote and Local).  The set point is selected by toggling the REMOTE input parameter.

The direction of the action of the function is chosen by the DIRECTN parameter.  If this parameter is true then the function will act in the same direction as the process value

The value connected to TSCAN should correspond to or be less than the cycle time of the task where the function block is used.

The INTLCK input parameter allows the function output to return to a known value (INTLCKV) if the parameter is true.  For example, if an error or alarm condition occurred the INTLCK value would be set high and the FPID function output would be set to the INTLCKV value.

## PID vs. FPID

Though both functions calculate the control output the in the same manner, the FPID function has more parameters for added functionality.  The main difference between the two functions is the limiting of the output.  The PID function does not inherently allow the user to limit the minimum and maximum of the output.  If for example, the process value (PV) were to dwell below the set point (SP), the PID function would compensate by continually increasing (in a reverse acting control loop) the function output.  The PID will continue to compensate the output value for as long as the process value stays below the set point.  In this situation it is possible for the mathematical output of the to exceed the physical output.  Similarly, if the PV stays below the SP for an extended period then suddenly increases to a value greater than the SP the function output will take longer to respond.  This situation is illustrated in the figure below.

The FPID function can inherently limit the mathematical output of the function.  Therefore, the function output can be limited to the actual physical output of the system.  If we examine the same situation described previously, the response time for the FPID output will be different.  This is described in the graph below.

In this situation the response time of the function output is greatly decreased.

# Text boxes

PV

SP

Time

Output Maximum

FPID Output

Time

PV

SP

Output Maximum

PID Output