Note: WorkStation Shell Uploads

Product:	PowerStations

Date:	3/1/02

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Guide to Project Management using IPM and PowerStations running the WorkStation Shell

Uploading an Interact project and downloading it to another PowerStation without making changes

- Preparing the PowerStation for project upload

- Your PowerStation must be in the Workstation Shell to do the upload. To exit Interact and return to the Workstation Shell, connect a keyboard to your PowerStation, hit F10 to bring up the Interact Application Manager. If you are at User Level 0 then you will have an EXIT INTERACT button. Otherwise use the CHANGE USER button go to User Level 0. EXIT INTERACT and ACCEPT in the next screen.

- You should now be at the Workstation Shell screen shown below. You must be in the Shell and not Interact for Interact Project Manager (IPM) transfers to work.

- If you have a PowerStation model P21-XXXXX that does not have a keyboard port, and your application does not have a “Go to AM” action button, then you can still download to the unit using the download button in the back of the unit. This button enables the PowerStation to send or receive a Project from the Interact Project Manager (IPM) even if the PowerStation was still running Interact. Pressing the download button displays the screen shown below. If a serial download cable is connected between your computer and the PowerStation, then project transfer will begin once the appropriate option is selected in IPM.

Pressing the download button a second time causes the PowerStation to reboot.

.

- Preparing the Windows PC for project upload

- Launch IPM using either the IPM.exe or the IPM.pif file in the C:\interact\ps directory

- Under the Transfer menu, configure the appropriate COM port. Then connect a serial cable from the appropriate COM port on the PC to the PowerStation. IPM uses a standard null-modem cable as shown on the next page.

- Uploading a project using IPM

- Go to the Transfer menu, then Make Backup and Backup Project from the Remote System

- IPM will prompt you for a path when the backup is finished.

- This will create a folder under the specified path with 2 zip files and a control.001 file

- If you do not wish to make any changes to the application, then you can proceed to download the project to the replacement unit using the Send Backup command as shown below:

- If you wish to edit the application before downloading it back to a PowerStation, you must first restore the project. Select Restore Backup to PC from the IPM Transfer menu.

- You will be asked if you wish to restore Interact. Choose No. If you agree to restoring Interact then you will overwrite the existing runtime files on your PC with potentially older versions.

- Once the restore is finished you need to open the project. You are now ready to edit the file in Interact.

- Run Interact using the Wam.exe file from your C:\Interact\Am directory.

- Open the Interact application as shown. Note that folder icons indicate projects while green icons denote applications.

- Once you have modified and saved your application, you can use IPM to send the project back down to the PowerStation.

- Installing Interact and IPM

- If you do not have Interact and IPM on your PC then you will need download them from our FTP site and install them. You must install Interact before you install IPM. Interact Version 5.21 Windows development is located at ftp://www.ctcusa.com/ctcsupport/Interact/Releases/Itr521/Windev/ .You can either download the 11 individual disks, In521_01.zip through In521_11.zip and extract them to 3.5” floppy disks or you can download the single setup file In521_Al.zip instead. If you choose to create the 11 floppy disks, you will have to label each of the individual disks Interact_1 through Interact_11

- Select In521_Al.zip and save the file on to your desktop.

- Once the file is downloaded, you can unzip the file by right clicking on it and selecting one of the extract options. Run the Setup.exe file to begin the Interact install.

- You are now ready to install IPM. You can download IPM from our website at ftp://www.ctcusa.com/ctcsupport/Interact/Releases/Itr521/IPM.  Download IPM_202.zip to the desktop and unzip it. You can run then run the IPMINST.exe file from a DOS prompt.

5. The Interact development installation added two set statements to your Autoexec.bat file. The IPMINST.exe file seeks out the directory specified by the SET INTERACT statement creates a PS directory and installs IPM within it.

- Moving the Flash SIMM from one PowerStation to another

Although the recommended method is to first upload a project backup using IPM (Interact Project Manager) and then send the project backup to the spare unit. You can also remove the Flash SIMM from the failed unit and install it in the backup.

WARNING:	Observe normal precautions against static discharge to prevent damage to your PowerStation or to your flash memory board. Also, use extreme caution when inserting flash memory into a socket or damage to the socket or memory board could result. Be careful to orient the board properly on the socket.

To install the flash memory, first turn off the PowerStation.

Next unscrew the four screws to remove the cover plate. The Flash SIMM connectors are located on the logic board at the location shown on the right.

Orient the Flash SIMM as shown below.

Angle the Flash SIMM into the socket.

Push the Flash SIMM onto the socket till the tab on the socket fits into the flash board hole.

Ensure socket ejectors are holding the Flash SIMM in place.

Secure the cover plate with the four removed screws and turn on the PowerStation.

- MachineShop Toolbar with Interact 5.x

    - IPM is a DOS based utility so it may not work under Windows NT or Windows 2000. If you cannot get IPM to work then you will need to install the MachineShop Toolbar instead. Download the 4 disk toolbar install from our FTP site at ftp://www.ctcusa.com/ctcsupport/MachineShop/Releases/Toolbar/MSPTB102

    - Unzip MSPTB102_All.zip to reveal 4 disk folders. Launch Setup.exe

3.  Install the Toolbar in the C:\Machshop directory

4. If you have any existing IPM projects, then the Toolbar install will convert them for you

- For more information on using the Toolbar with Interact 5.x refer to document 0047.DOC - Using the MachineShop Toolbar with Interact 5.X at http://www.ctcusa.com/ctcnet/Support/AppNote.asp#MS. For more information on uploading from a PowerStation using the IPM Compatible Transfer in MachineShop Toolbar, refer to 0084.DOC at the same link.