Note:	P1X-PWRAC Specification

Product: P1X-PWRAC

Date:	11/19/02

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# P1X-PWRAC and BKT-1000 Specifications and Details

General Specifications:

Input voltage  ………………………….….90VAC to 260VAC

Input frequency  ………………………………...47Hz to 63Hz

Inrush current  ……………< 60A at 230VAC Cold start, 25 oC

Output voltage  …………………………………...+23V~+25V

Output current rating (continuous)……………………..…2.3A

Efficiency  …………………………….….>70% at full current

Hold up time  …………….. > 16ms at rated load and 115VAC

Over voltage protection  …………………………….. latch-off

Short circuit protection  ……………………….. auto recovery

Over load protection  ………………………….. auto-recovery

Operating temperature  ……… …………………… 0 to 50 oC

Cooling ...............................…. …………... free air convection

Storage temperature.................…………….... -40 oC to +85 oC

EMI .............................…...........…..……………. FCC class B

Safety ................ UL 1950 D3, CSA 22.2 No.234, VDE 60 950

Mechanical Specifications:

BKT-1000:

The kit includes the following:

- Three mounting brackets

- Two black gaskets

- Mounting hardware (screws)

- One mounting template

- Mounting instructions

Mounting template (not to scale):

BKT-1000 Mounting Example: