50 West TechneCenter Drive • Milford, OH 45150

Voice: (513) 248-1714 • Fax: (513) 831-5042

Internet: http://www.ctcusa.com/

COMPUMOTOR – GEMINI

UDI DRIVER

Version 1.2

User Guide Version 1.11

Schmoll

CTC Parker Automation

Application Engineering

50 W. TechneCenter Dr.

Milford, OH 45150

# Disclaimer Notice

Copyright (C) 2001 by CTC-Parker Automation. All rights reserved. No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, in any form or by any means, mechanical, photocopying, recording or otherwise, without the prior written consent of Computer Technology Corporation. While every precaution has been taken in the preparation of this manual, Computer Technology Corporation and the author assume no responsibility for errors or omissions. Neither is any liability assumed for damages resulting from the use of the information contained herein.

Trademarks

All product and company names are trademarks of their respective companies and licenses.

CTC Parker Automation

50 W. TechneCenter Drive

Milford, OH 45150-2739

(513) 831-2340

Technical Support (513) 248-1714

# Table of Contents

Disclaimer Notice	2

Table of Contents	3

1.	Introduction	4

1.1 Requirements	4

1.2 Driver Installation	4

2.	GEMINI DRIVER SETUP	5

2.1 Command List…………………………………………………………………………………5

2.2 Read/Write Implementation………………………………………………………………….6

2.3 Addressing Format……………………………………………………………………………7

3.	AutoEXEC Setup	8

3.1 Creating an Autoexec.bat in the Startup directory…………………………………………8

4.	aDDDITIONAL INFORMATION	8

# 1. INTRODUCTION

This document describes the Compumotor UDI Driver developed by CTC Parker Automation.  This driver was designed to interface with the Gemini Series controllers.

#### 1.1 Requirements

This driver was developed with Microsoft C version 6.0.  It interfaces with Interact version 6.0’s UDI driver.

Interact’s on-line help selectable in the UDI Driver’s setup dialog will be an important supplement to this document.  Familiarity with Interact and the UDI driver will therefore be of great advantage.  It is also important to be familiar with the Gemini’s communications protocol, DOS and Windows.

#### 1.2 Driver Installation

Copy the Gem.exe file to the C:\MachShop\Projects\Interact\<Project>\Startup directory, where <Project> is the name of your project.  When you open your project the following window will appear.  Select the Gem.exe file then click “Open”.

The Gemini UDI driver is now installed in your project.

# 2. GEMINI DRIVER SETUP

#### 2.1 Command List

| Command | Description | Start Offset | Block Length | Read/Write |
| --- | --- | --- | --- | --- |
| RUN | Executes a defined program | *See Note* | 1 | Write |
| A | Acceleration | 1 | 1 | Read/Write |
| V | Velocity | 1 | 1 | Read/Write |
| D | Distance | 1 | 1 | Read/Write |
| GO | Initiate a motion command | 1 | 1 | Write |
| K | Instructs the drive to stop motion | 1 | 1 | Write |
| MC | Preset/Continuous Mode Enable | 1 | 1 | Read/Write |
| MA | Absolute/Incremental Mode Enable | 1 | 1 | Read/Write |
| S | Stop motion | 1 | 1 | Write |
| RESET | Similar to a power cycle | 1 | 1 | Write |
| LJRAT | System Load-to-Rotor/Force Inertia/Mass Ratio | 1 | 1 | Read/Write |
| OUT | Output Control | 1 | 1 | Write |
| HOM | Go Home | 1 | 1 | Read/Write |
| HOMV | Home Velocity | 1 | 1 | Read/Write |
| VARI | User Variable | *See Note* | 1 | Read/Write |
| DRIVE | Drive Enable | 1 | 1 | Read/Write |
| TSS | Transfer System Status | 1 | 4 | Read |
| TIN | Transfer Input Status | 1 | 1 | Read |
| TOUT | Transfer Output Status | 1 | 1 | Read |
| TAS | Transfer Axis Status | 1 | 8 | Read |
| TPC | Transfer Position Command | 1 | 1 | Read |
| TPE | Transfer Position of Encoder/Resolver | 1 | 1 | Read |
| TPER | Transfer Position Error | 1 | 1 | Read |
| TINO | Transfer Other Input Status | 1 | 1 | Read |
| TDHRS | Transfer Operating Hours | 1 | 1 | Read |
| TMTEMP | Transfer Motor Temperature | 1 | 1 | Read |
| TDTEMP | Transfer Drive Temperature | 1 | 1 | Read |
| TTRQA | Transfer Actual Torque/Force | 1 | 1 | Read |
| TER | Transfer Error Status | 1 | 4 | Read |
| TERRLG | Transfer Error Log | 1 | 512 | Read |

2.2 Read/Write Implementation

All commands must be set up in the Read and Write block tables.  Begin the driver configuration by inserting the commands in the appropriate table.  Some commands will be set up in both tables.  Determine the offset and block length from the table in section 2.1 of this document.  The station number should correspond to the station list.  Write buffering can be left at its default.

*Note:  For the “RUN” command the “Start Offset” will always be one.  Simply place the program number to be run in this variable.  Example using the set button place a ‘4’ in the value and place a UDI\0:RUN1

Note:  VARI:  The GEM is programmed to allocate each VARI separately.  For each VARI desired enter the number of the var in the read or write section of the configuration.  The offset for any VARI command will always be ‘1’.  I.e. if VARI22 is desired a separate read configured for VARI will be setup with the offset of 22 and a block length of 1 set in the configuration.

#### 2.3 Addressing Format

The following is the addressing format used for the Gemini UDI driver:

##### UDI\0:TPE1

When addressing Interact tools to the TSS, TIN, TOUT, TINO, TAS, TER, or TASX commands refer to the following table:

| Command | Gemini Bit Reference | Corresponding Interact Address Reference |
| --- | --- | --- |
| TAS | 1 – 8 | UDI\0:TAS1.1 – UDI\0:TAS1.8 |
|  | 9 – 16 | UDI\0:TAS2.1 – UDI\0:TAS2.8 |
|  | 17 – 24 | UDI\0:TAS3.1 – UDI\0:TAS3.8 |
|  | 25 – 32 | UDI\0:TAS4.1 – UDI\0:TAS4.8 |
| TER | 1 – 8 | UDI\0:TER1.1 – UDI\0:TAS1.8 |
|  | 9 – 16 | UDI\0:TER2.1 – UDI\0:TAS2.8 |
|  | 17 – 24 | UDI\0:TER3.1 – UDI\0:TAS3.8 |
|  | 25 – 32 | UDI\0:TER4.1 – UDI\0:TAS4.8 |
| TAS (TASX) | 1 – 8 | UDI\0:TAS5.1 – UDI\0:TAS5.8 |
|  | 9 – 16 | UDI\0:TAS6.1 – UDI\0:TAS6.8 |
|  | 17 – 24 | UDI\0:TAS7.1 – UDI\0:TAS7.8 |
|  | 25 – 32 | UDI\0:TAS8.1 – UDI\0:TAS8.8 |
| TSS | 1 – 8 | UDI\0:TASS1.1 – UDI\0:TASS1.8 |
|  | 9 – 16 | UDI\0:TASS2.1 – UDI\0:TASS2.8 |
|  | 17 – 24 | UDI\0:TASS3.1 – UDI\0:TASS3.8 |
|  | 25 – 32 | UDI\0:TASS4.1 – UDI\0:TASS4.8 |
| TIN | 1 – 8 | UDI\0:TIN1.1 – UDI\0:TIN1.8 |
| TINO | 1 – 8 | UDI\0:TINO1.1 – UDI\0:TINO1.8 |

Note 1: Gemini -TASX commands are implemented using the TAS bytes 5 through 8.  If the address TASX1.1 is desired the user should address it as TAS5.1.

# 3. AUTOEXEC SETUP

#### 3.1 Creating an Autoexec.bat in the Startup directory

In order for the Gem.exe file to load in runtime an Autoexec.bat file must be created to call the executable and configure it correctly.  Use Window’s Notepad to create this file and store it to the C:\Startup directory of the Compact Flash of the PowerStation.  The Autoexec should contain the following text:

C:\STARTUP\GEM.EXE

This Autoexec uses the default of COM port 1 at a baud rate of 9600 with no parity, 8 data bits, and 1 stop bit.  If another configuration is desired use the following format:

GEM [/i int] [/c commport, baud, parity, databits, stopbits, IRQ]

/i = set interrupt number 60h - 67h

/c = communication parameters:

commport = 1 - 4

baud     = baud rate (up to 115200)

parity   = N, E, O (none, even, or odd)

databits = 5, 6, 7 or 8

stopbits = 1 or 2

IRQ      = 2, 3, 4, 5, 6, 7

Example: GEM /i 62 /c 4, 9600, n, 8, 1, 5

# 4. ADDITIONAL INFORMATION

Due to the ANSI/IEEE (Std 754-1985) 24 bit single floating point data type standard, numeric information can only be accurate to 7 decimal places.  More data can be stored, but precision can only be guaranteed to the 7th decimal place.

# Text boxes

Driver Name

Station Number

Command

Start Offset