Note:	P3-P7_Networking

Product:	 P3/4/5/7 PowerStations

Date:	2/26/99

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Networking Setup for the P3 through P7 PowerStations

Go to the C:\NET directory on the PowerStation and run the RSET8019 or AT5CFG utilities to identify the I/O port and IRQ assigned to the Ethernet port.  One of these Ethernet port configuration utilities will be present in the C:\NET directory.

AT5CFG:

- Connect a keyboard to the unit using the Y-Adapter. (The P5 does not need the Y-Adapter to connect the keyboard)

- Exit to the DOS Shell from the WorkStation Shell Main Menu.

- Change to the C:\NET directory.  Type in AT5CFG.EXE and hit the ENTER key.

- The AT5CFG Utility will state, in the ADAPTER window, what the configuration of the I/O port and IRQ are.

RSET8019:

- Connect a keyboard to the unit using the Y-Adapter. (The P5 does not need the Y-Adapter to connect to the keyboard)

- Exit to the DOS Shell from the WorkStation Shell Main Menu.

- Change to the C:\NET directory.  Type in RSET8019.EXE and hit the ENTER key.

- When the RSET8019 Utility runs hit the SPACEBAR.

- The I/O port and IRQ configuration will be shown in the window.

Hardware:

- Put the PowerStation in the WorkStation Shell Main Menu.

- Connect the download cable to a COM port of the P3 through P7.

*Note:  Be sure that the COM port is enabled for a download in the WorkStation Shell and    configured for RS-232 communications.

- Using a computer with the Interact Project Manager (IPM) utility, enter Super User Mode to access the PowerStation flash.

- Boot into DOS on the PC.

- Change directories to the C:\Interact\PS directory.

- Type in IPM and hit the ENTER key.

- Go to Settings and confirm that Super User Mode is On.

- Go to the DOS menu command.

- Select Visit DOS, then select C:\ Local Hard Drive.

- IPM will switch to a DOS screen.  Look for the statement that assigns a drive letter                              to the PowerStation flash disk.

- Change to the drive letter assigned to the PowerStation flash disk.

- Type in EDIT AUTOEXEC.BAT and press ENTER.

- Towards the end of the batch file look for the line REM  C:\NET\NET.BAT.

- Remove the REM statement and replace it with CALL.  If CALL already appears in the statement, just remove the REM.

- Hit the keys “Alt” and “F” and select SAVE.

- Hit the keys “Alt” and “F” again and select EXIT.

- Change directories to the C:\NET directory.

- Edit the NET.CFG file.

- Make sure that the IRQ is set to 10 and the I/O port address is set to 280 Hex.

- Save and Exit the file.

- Reboot the PowerStation.

- The Ethernet port is now active.  This completes the hardware setup.

Software:

- To configure the NBIOS driver, start the Interact Development software in Windows95/NT.

- Open your application and select Drivers Used under the Application Manager.

- Select NetBios Network Driver from the list.

- Select <<ADD.  Then select OK at the bottom of the property sheet.

- At the bottom of the Application Browser window, double click on the Netbios Network Driver.

- The property sheet for the NetBios Networking Driver (NBIOS) will open up.

- Give the NBIOS driver a unique network Node Name.

8.    This completes the software setup.