Note:	Create a Bar Graph with GMM

Product:	Interact - GMM

Date:	12/12/95

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

To Create a Bar Graph in GMM:

1.	Draw a rectangle to maximum size desired.

2.	Connect Object:

a.	Motion	-	Reference an address to be monitored

Set MIN and MAX values

Press XY for Size and Location Control

Press MINIMUM

Click on rectangle and size down for minimum

b.	Appearance  -	Add a connection (reference address) for every color stage of the rectangle.

Change the foreground color for every connection

EXAMPLE:

Motion Connection

Ref:	DVR\1:2 (demo driver address to monitor)

Min:	0

Max:	100

Apply Connection:	Always

Size Control:		XY

Location Control:	XY

Note:  Pay attention to where object is at Max and Min.

Appearance Connection

Ref:	1)  Address > 0

Foreground color:  Green

2)  Address > 25

Foreground color:  Yellow

3)  Address >75

Foreground color:  Red

That’s all.  Execute either TEST or RUN Mode and verify.

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.   w   Milford, OH  45150
Phone (513) 831-5042   w   Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com   w   E-Mail:  support@ctcusa.com