Note: Additional Ethernet Adapter

Product:  P1 or P2 (PC104)

Date:	  10/23/00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Adding a PC104 Ethernet Adapter to a P1 or P2

Introduction

This application note will provide information on how to configure a PC104 Ethernet adapter to a P1 or P2 PowerStation.

*Note: See your PowerStation guide for information on how to install a PC104 card to your unit.

Selecting An Ethernet Adapter

When selecting a PC104 Ethernet Adapter for a PowerStation, be sure that your card is DOS configurable - not “Plug and Play”, and NE2000 compatible.  Also, when selecting an adapter choose one with an AT\LANTIC Ethernet controller.  This card is available from WinSystems (part number: PCM-NE200).

P1 Configuration

After you have installed the card on the P1, copy the Default.exe file from the diskette provided with your card to the C:\Net directory of your Flash card.  Next, re-insert the Flash into the P1, and connect a keyboard to your unit.  Now power on the P1 and be continually pushing the F5 key on your keyboard.  By pushing the F5 key you will interrupt the boot process.  Also, you may need to use the Alt+Arrow keys to scroll around the ¼ VGA screen.  Once you have a C: prompt, type the following commands:

- CD\NET

- DEFAULT

- AT5CFG

The Default utility will re-configure the EEPROM on the card for an available Port Address and IRQ.  The AT5CFG command will launch the configuration utility for the card.

In the AT5CFG utility select Change Adapter Configuration.  Use the Tab button to change the I/O port address to 300, then press Enter.  Now use the Tab button to change the IRQ of the card to 5.  This IRQ is usually available if you have not installed any other devices to your P1.  Now scroll down to Save Configuration, and press Enter.  Ignore any error messages, and quit to DOS.  Now cycle power on the unit.  The new Ethernet adapter is now configured and available.

P2 Configuration

After you have installed the card, power the unit on.  From the MachineShop shell, exit to DOS.  Type the following commands:

- CD\NET

- AT5CFG

In the AT5CFG utility select Change Adapter Configuration.  Use the Tab button to change the I/O port address to 300, then press Enter.  Now use the Tab button to change the IRQ of the card to 5.  This IRQ is usually available if you have not installed any other devices to your P1.  Now scroll down to Save Configuration, and press Enter.  Ignore any error messages, and quit to DOS.  Now cycle power on the unit.  The new Ethernet adapter is now configured and available.