# MachineShop Download Quickstart Guide For Serial Transfers to the Workstation (Powerstation) Shell (IPM Compatible)

This Quickstart Guide was designed by the CTC Training department to assist customers with MachineShop Download functions. While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

The MachineShop Toolbar

The IPM Compatible (Serial) Connection is a transfer method that allows you to send projects to   PowerStations running the old PowerStation Shell. The MachineShop Toolbar replaces the old IPM utility.

Launching MachineShop and selecting a project to download:

- Start MachineShop by double-clicking the MachineShop desktop icon or choosing the Windows Start, Programs, MachineShop, MachineShop Toolbar.

- Choose the MachineShop ‘File’ menu.

- Choose ‘Open Project…’ and select the MachineShop project you want to download.

- Choose the ‘Open’ button. After selecting the project, the project name will be displayed in the upper right-hand corner of the toolbar.

MachineShop Toolbar

Part 1

Adding a connection:

If you have already configured a connection and have previously downloaded, go to Part 2.

Before transferring, you must define a Transfer Connection. This is how you will transfer files to or from the runtime system. The Transfer Wizard will allow you to quickly configure the connection.

To create a MachineShop connection with the Connection Wizard:

- Choose the Connection Wizard icon from the MachineShop toolbar. This is displayed to the left of the Transfer Connection Window.

Transfer Wizard icon and Transfer Window

- Choose the ‘Download to Runtime’ option on the Transfer Wizard. Download defines data that is being transferred to the PowerStation while Upload defines information coming from the PowerStation.

Transfer Wizard Step 1

- Choose ‘Next’.

- Choose ‘Define New Connection’. This will display the Add Connection Menu.

Defining a Connection Name

- Type a connection name. This will create a name for your connection so you may want to type a descriptive name such as ‘SERIAL’.

- From the Connection type pull down menu, choose IPM Compatible (Serial).

- Choose ‘OK’

Serial Communication Parameters

- Select the proper Com port on your PC and choose ‘Finish’.

Part 2

Configuring the PowerStation for Serial Download:

- Turn on the PowerStation.

- Access the PowerStation Shell Main Menu.

Note:

If you are currently in INTERACT, exit to the Shell Main Menu. There are several ways to exit the INTERACT program. If this action was programmed using a Function Key, you may want to write down the Function Key that exits INTERACT here:

Function Key: ____________

- From the Workstation Shell, select ‘CONFIG SETTINGS’.

- Choose ‘SET HARDWARE’.

- Select ‘DOWNLOAD ENABLE’ and make sure the COM1 and COM2 ports are set to YES.

- Connect a serial cable between the PowerStation and PC. The following diagram shows you how to make a serial cable with loop back capability that has a 9-pin or a 25-pin female connector at either end.

Part 3

Downloading to the PowerStation:

If you do not have a connection in your pull down list named ‘SERIAL’, go back to Part 1.

- In the MachineShop Toolbar, make sure the connection named ‘SERIAL’ appears in the window as shown in the following menu. This is the connection you previously created.

Choosing a Connection

- Choose ‘Next >’.

- Depending on what you are transferring will determine how the following menu will be configured. (See below)

Selecting Transfer Options

If you want to overwrite the current project on the PowerStation or you are transferring to a PowerStation that does not contain a project, check the ‘Complete Project’ checkbox.

Note:

If you want to transfer specific components of a project you can uncheck the ‘Complete Project’ checkbox and choose any combination of the following:

Program Files – choose this option if you want to update or add an additional Interact module or driver to an existing project on the PowerStation.

Application Files – choose this option to transfer user created files. (Panels, alarm configuration files, etc.)

Startup Files – choose this option to transfer files that are located in the startup directory for your project.

For faster transfers, you may want to check ‘Updated Files Only’. This will send only files that have been modified since the last transfer.

4. Choose ‘Finish’. The files will now transfer to the PowerStation.

Transfer Status Screen

- When the project has transferred, choose ‘Close’.