Note:	MCM handshaking

Product:	Interact

Date:	3/19/02

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Verifying downloads in MCM using the ‘Download Complete’ input and ‘Accept Download’ output

- You can verify that your MCM list was successfully downloaded to the controller by configuring the ‘Download Complete’ input and ‘Accept Download’ output fields in MCM Group Properties. Open up a list in MCM then choose the File menu, Group Properties, select your group and press OK to bring up the Group Properties window. Select Cancel when finished.

- Go to the Controls tab of the Properties window. Select the Help button to launch the Machine Configuration Module Help screen to read up on each of the options on that screen.

- The Controls tab is shown below:

- Configure the two tags in your PLC logic as follows. The ‘Download Complete’ input @dlcomplete, will turn on the ‘Accept Download’ output @dlaccept. This will cause the MCM module to then reset @dlcomplete.

- As long as this PLC handshaking occurs before the List Timeout value is reached then the download was successful. If the timeout value is reached then the Download/Upload Error Message will appear.

- A sample Interact screen is shown below

- The remote message display tool set to MCM\msg_display will display the Download/Upload Error Message if there are problems with the download. If the download is successful then both the @dlcomplete and @dlaccept bits will toggle on.