# Note:   Pwrstn to AIC for DH485com

Product:	Interact

Date:	11-6-00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Connecting a Powerstation via COM2 to an AB 1747-AIC Module for Communication on a DH485 network of PLC’s.

Note:  This appnote assumes that COM2 of the powerstation has been left at its factory default settings.  Consult the User’s Guide if you needs to change the Com2 jumper settings to reflect the RS-485 Communications protocol.

The SLC500 processors Channel configuration MUST be set for DH-485 Master.

Following diagram shows the pinout that will be used to communicate to the DH-485 Interface.

You have the option of Daisy-Chaining several 1747-AIC modules together via this Cable diagram.

Any Powerstation that has a 25pin COM port WILL be able to communicate directly to the Peripheral Port on the AB 1747-AIC module using the supplied pinout in the SLC5 driver help file.

The following diagram displays a valid configuration for Connectivity on a DH-485 Network to multiple PLC’s.