Note:	Downloading and Backing

Up a Project

Product:	P2, P3, P5

Date:	12/12/95

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Creating and Downloading a Project to a Powerstation

1.	Make sure Interact software and the Interact Project Manager are installed on your PC, then connect the 	serial download cable between the PowerStation and your PC.

2.	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is 	C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

3.	Choose the Projects menu by clicking on the word Projects or pressing P on the keyboard.

4.  	To create a new project, choose New Project.  You will be prompted to type in a project name, then press 	ENTER.

5.	Now choose Copy Application from the Projects menu.  You can copy an application from an existing 	project or from the Interact Appfiles subdirectory.  To copy an application, highlight the name using the 	arrow keys and press ENTER.  You may copy as many applications as you want to into the project.

6.  	Use the right arrow to move to the Settings Menu.  Choose either Development or Runtime, depending on 	what you want to download.  Verify that the total file size listed on the screen will fit into the storage

memory available on the PowerStation.

7.  	Use the right arrow to move from the Settings Menu to the Transfer Menu.  Choose Transfer Settings, and 	then select the COM port you will downloading from.  Choose the fastest baud rate that your PC can handle.  	Most PCs will be able to use 115200 baud.

8.  	Make sure the PowerStation is on and at the Shell menu (not at the Interact Application Manager menu).

9.  	Back on your PC, use the up arrow key and choose Send Project.

Downloading an Existing Project to a Powerstation

1.  	Make sure Interact software and the Interact Project Manager are installed on your PC, then connect the 	serial download cable between the PowerStation and your PC.

2.  	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is

C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

3.  	Choose the Projects menu by clicking on the word Projects or pressing P on the keyboard.

4.  	Choose Open Project, then highlight the project name you desire (using arrow keys) and press ENTER.

5.  	Use the right arrow to move to the Settings Menu.  Choose either Development or Runtime, depending on 	what you want to download.  Verify that the total file size listed on the screen will fit into the storage

memory available on the PowerStation.

6.  	Use the right arrow to move from the Settings Menu to the Transfer Menu.  Choose Transfer Settings, and 	then select the COM port you will downloading from.  Choose the fastest baud rate that your PC will handle.  	Most PCs will be able to use 115200 baud.

7.  	Make sure the PowerStation is on and at the Shell menu (not in Interact).

8.  	Back on your PC, use the up arrow key and choose Send Project.

Sending Only an Application to a Powerstation

1.  	Connect the serial download cable between the PowerStation and your PC.

2.  	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is

C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

3.  	Choose the Projects Menu by clicking on the word Projects or pressing P on the keyboard.

4.  	Choose Open Project, then, using the arrow keys, highlight the project name that matches the current 	project on your PowerStation and press ENTER.  (You may only send applications from the current 	PowerStation project you are downloading to, not from a different project)

5.  	Make sure the PowerStation is on and at the Shell menu (not in Interact).

6.  	On your PC, use the right arrow to move to the Transfer Menu.  Choose Send Application.  Highlight the 	desired application and press ENTER.

Creating a Backup of Your Project from a Powerstation

1.  	Connect the serial download cable between the PowerStation and your PC.

2.  	Make sure the PowerStation is on and at the Shell menu (not at the Interact Application Manager).

3.  	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is

C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

4.  	Choose the Settings Menu, and then choose Archive Path.  On the "Backup To" line, type in the path 	where the backup will be stored.  For example, to backup your project to a floppy disk, type in A: and press 	Enter.

5.  	Use the right arrow key to move to the Transfer Menu.  Choose Make Backup, then choose Backup 	Project From Remote Workstation.  The PowerStation will restore all of the files to your PC (temporarily 	stored in RAM), then prompt you again to let you change the backup path if you want to.  If you don't make 	any changes to the backup path when prompted, press ENTER and the file will be sent to the original path 	you specified under Archive Path.

Restoring the Backup from a Floppy Disk to Your PC

1.  	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is

C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

2.  	Insert the backup disk into the disk drive (A:, B:, etc.)

3.  	From the Project Manager, choose Transfer Settings and then choose Restore Backup to PC.

4.  	You will be prompted for the Restore From path.  Type in the floppy drive where your backup disk is 	located.  For example, if you are restoring a project from a disk in the A: drive, type A:\ in the blank, and 	then delete the rest of the path.  The blank should now read A:\.

5.  	When you are asked if  you want to restore from A:\, press ENTER for yes, then you will be prompted to 	choose which project from A: you would like to restore.  Use the arrow keys to highlight your project and 	press ENTER.

6.  	You will now be asked if you would like to restore Interact.  If you already have Interact on your system, you 	can choose NO.  If Interact software is not already installed on your PC, choose YES.

7.  	Now the project has been restored to your PC.  To load the project, go to the Project Menu and Open 	Project.  Follow the steps to Downloading an Existing Project to the PowerStation to download the 	restored backup.

Restoring the Backup from a Floppy Disk to a Powerstation

1.  	On the PC, go to the directory where the Interact Project Manager is installed.  The default path is

C:\INTERACT\PS.  Type IPM.  This will bring up the Project Manager.

2.  	Insert the backup disk into the disk drive on your PC (A:, B:, etc.).  Be sure the PowerStation is at the Shell 	menu and not in an Interact Application.

3.  	From the Project Manager, choose Transfer Settings and then choose Send Backup.  When prompted for 	the Restore Path, type the drive where your backup file is held.  For example, if you are restoring a project 	from A:, type A: in the blank and press ENTER.  You will be asked if you want to send the backup from A:, 	press ENTER for YES.

4.  	You will be prompted to select the name of the project to be sent.  Use the arrow keys to select the project 	and press ENTER.  Now you will get the following message:  “Sending a Backup will force the remote 	workstation to reset and overwrite all existing data.  Do you wish to continue?”  Press ENTER for YES.

Your project will now download to the PowerStation.

Restoring the Backup from a PCMCIA Card to a P3 or P5 Powerstation

1.  	Insert the PCMCIA card (with the backup file on it) into the PCMCIA slot on the back of the PowerStation.

2.  	Press the white button labeled 'Interact' (on the back of the PowerStation) once.

3.  	Follow the directions on the screen of the PowerStation to "restore an archived project from the PCMCIA 	drives to the system drive B:"   On a touchscreen, there will be an area on the screen to touch in order to 	restore the project.

4.  	The PowerStation will then search the PCMCIA card for backup projects, and allow you to select which 	backup to restore.

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.   w   Milford, OH  45150
Phone (513) 831-5042   w   Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com   w   E-Mail:  support@ctcusa.com