Note:	AB_M-LOGIX-1500_ser

Product:	Interact

Date:	12-28-00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# MicroLogix 1500 Serial Connectivity using the ABDH drv.

The MicroLogix processor lets you operate DF1 communication protocol by means of the RS-232 communication port.

Note:   When using the Allen-Bradley Data Highway driver with any Allen-Bradley MicroLogix model of controller, make sure that the System Mode Driver configuration settings are set to:

DF1, FULL DUPLEX, and set the error detection to BCC.

To communicate with the MicroLogix controller use the Allen-Bradley PC cable supplied with the controller.  (Part number: 1761-CBL-PM02)

## DRIVER CONFIGURATION

You MUST select SLC5 for the PLC Type in the Drivers Configuration as shown below.  The MICRO option is selected only when you are using MicroLogix1000’s.