Note: Recovering Compact Flash

Product:	Compact Flash

Date:	9/23/02

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Recovering Compact Flash Cards using the SanDisk Imagemate Initialization Utility

- CTC Parker Automation provides the FlashBack utility for initializing and recovering Compact Flash cards. If the FlashBack does not recover your compact flash however, then you will need to use an alternate utility by SanDisk before rerunning the Flashback utility.

- This SanDisk utility is for USB Compact Flash readers (part number SDDR-31) in Windows 98 only. You can download this utility off their website at the following link. http://www.sandisk.com/tech/31.asp The utility can be run from the Start menu as seen below. Select Initialize and then Quick.

- Once you have completed running the SanDisk utility, run the CTC FlashBack utility. If the compact flash card still does not boot in your PowerStation then you will need to purchase a new flash card. New compact flash cards should be initialized using FlashBack.

- Compact Flash cards can get corrupted if they are removed from a USB reader in Windows 2000 prematurely. Always wait at least 1 minute before removing the Compact Flash from the USB reader in Windows 2000.