Note:	Peer-to-Peer_Networking

Product:	PowerStations

Date:	12/18/1998

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# Peer-to-Peer Networking with a PowerStation to PC to Map a Remote Drive for Interact Logging

Note:  For this procedure, use the Windows for Workgroups 3.11 DOS client files to login to the network and map a drive on a Peer Windows 95 PC.  It is the end user’s responsibility to obtain these files and properly load them given their existing network and requirements.  The presence and input of the Network Administrator is recommended.

Procedure:

- Transfer the WFWG DOS client files to the C:\NET directory on the PowerStation.

- Edit the NET.BAT file in the C:\NET directory to correspond to the included Net.Bat file.

- You will need to adjust the NET LOGON line and the NET USE line in the Net.Bat file for your particular network.  Talk to your Network Adinistator.

- Edit the Autoexec.bat file in the root of the C:\ drive on the PowerStation to match the highlighted sections of the included Autoexec.bat file.

- Connect the PowerStation and the PC together using either a hub with standard Ethernet cables or point-to-point using an Ethernet crossover cable.

- On the Windows 95 PC, be sure you have the Windows Network Client loaded.  Talk to your Network Administrator.  You will need to know the name of the PC on the network.  (Located in the Network Setup of the PC)

- Restart the PowerStation.

- At this point, the drive on the Peer Windows 95 machine will be mapped and accessible to the PowerStation in DOS.  (At a DOS prompt, try switching to the mapped drive letter)

Drivers:

WFWG Files:

Net.cfg		Net.exe		Shares.pwl			Dkappes.pwl

Net.msg		Neth.msg		Wfwsys.cfg			Share000.pwl

System.ini		Connect.dat		Net.txt

## Network Card Driver:	NE2000.com

Novell DOS Client Files:

Net.bat		Ipxodi.com			Lsl.com

#### Net.bat

## LSL

NE2000

IPXODI

NET LOGON   /Y

## NET USE E: \ \ PC_NAME\ PC_DRIVE /Y

### Autoexec.bat

@ECHO OFF

PROMPT  $P$G

SET TEMP=C:\DOS

PATH C:\;C:\DOS;C:\CTC;C:\NET   <- Add this underlined statement

## REM  ******************************************************************************

REM  Install PowerStation Special Functions

REM  ******************************************************************************

LH  C:\CTC\BIOSTSR

REM  ******************************************************************************

REM  If an external mouse is connected, MOUSE will install successfully, and NOMOUSE will do REM  nothing.  If external mouse is not found, MOUSE will fail, and NOMOUSE will successfully

REM  load.

REM  ******************************************************************************

LH  C:\CTC\MOUSE

LH  C:\CTC\NOMOUSE

REM	******************************************************************************

REM	Install TouchBase touchscreen drivers

REM	******************************************************************************

SET	TBDPATH=C:\TOUCH

SET	TBDINT=61

LH	C:\TOUCH\TBDRIVER /A:310  /I:15

LH	C:\TOUCH\TBMOUSE 1

REM	******************************************************************************

REM	Set up Interact environment variables for CTC shell

REM	******************************************************************************

SET	INTERACT=C:\INTERACT

SET	INTERACT_FILES=C:\INTERACT\APPFILES

SET	INTERACT_STARTUP=C:\STARTUP

REM	******************************************************************************

REM	Call AUTOEXEC.BAT file contained in project, if it exists

REM	******************************************************************************

IF   	EXIST C:\STARTUP\AUTOEXEC.BAT  CALL  C:\STARTUP\AUTOEXEC.BAT

REM	******************************************************************************

REM	Uncomment next statement to load network batch file

REM	******************************************************************************

CALL	C:\NET\NET.BAT

REM	******************************************************************************

REM	Start the CTC Shell

REM	******************************************************************************

CD	\CTC

PSU