Note:	Adding Fourth Com Port

Product:	P3-P7 Serial Tscreen Dvr

Date:	10/29/1999

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

The development software is only able to choose the four standard com port addresses for its comports (Com 1: 3F8 Hex, Com 2: 2F8 Hex, Com 3: 3E8 Hex, Com 4: 2E8 Hex).  The serial touchscreen  driver (SC3Dox) is only configurable for the same four standard comport addresses.  The Run-Time Application Manager allows a non-standard comport address to be chosen.  This capability is what allows the user to add a fourth hardware comport for serial communications.

- To install a fourth com port on a Powerstation P3-P7 you will need the following: B & B Electronics RS-232/422/485 Serial Card model #: 3PXCC1A or 3PXCC2A, keyboard (AT style w/Y-cable adaptor or PS/2 Style) and a mouse (optional).

- The manual (Document #: 3PXCC5098) that comes with the card will explain how to configure it to match the needed serial communication protocol.

- You will need to select a non-standard com port address (you will find examples of these on p. 6 of the manual) and an unused IRQ.  It is vitally important to choose a Base Hex Address (com port address) and an IRQ not used on your system otherwise you will get hardware conflicts and this will prevent usage of the card.

- Once the jumpers have been set for the needed communication protocol, com port address and IRQ, install the card observing proper Static Discharge Precautions (grounding straps, etc.).

- Boot the Powerstation and go into the Interact Application Manager.  Make sure your are in Program mode.  Your current mode is displayed in the lower left hand corner of the Interact Application Manager display window (above the 2 rows of buttons).

- Go to App Settings, Startup Settings and Com Ports.

- Click on or touch the port address for Com 4.  Type in the desired com port address (same as the setting for the B&B card).

- Repeat for the com port IRQ.

- Hit previous menu until you are back at the main menu.

- Go into Run Mode by touching the Run/Program button.

- Hit Go To Module button and choose PTM to enter your application.

- The setting for Com 4 will remain the same as long as you don’t go into the Com Port settings in the development software.

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.      Milford, OH  45150
Phone (513) 831-5042      Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com      E-Mail:  support@ctcusa.com