Note:	P2 5x86 Com 2 Configuration

Product:	Powerstation P2

Date:	9 March, 1999

# Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

- Locate Jumper 39.  It is approximately two (2) inches to the left and two (2) inches down from the top right corner of the card (see figure 1).  Pin one (1) is the top left pin in the six (6) pin configuration.  Set it according to the figures below for the communication protocol that is required.

- Locate Jumpers 35, 36, 37 and 38.  They are clustered approximately one (1) inch to the left and two (2) inches down from the top right corner of the card (see figure 1).  For all jumpers, pin one (1) is the top most of the three (3) pins.  Jumpers 35, 36 and 37 are the top most three (3) jumpers.  Jumpers 38 and 28 are below these jumpers.  Jumper 38 is the inside jumper and 28 is the one closest to the edge of the board.

NOTE: Jumper 28 is not to be changed.  Changing this jumper may cause display problems.

Set Jumpers 35, 36, 37 and 38 acccording to the figures below for the communication protocal that is        required.