Note:	Converting from an Unsigned Integer to a Signed Integer in Interact

Product:	Interact

Date:	12/12/95

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Display Output from the PLC:

To convert an unsigned integer to a signed integer, use the following formula in the display output address reference field:

(ADR-65536)+((ADR<=32767)*(65536))

Write Input to the PLC:

The Shortest Distance Between Man and Machine

50 W. TechneCenter Dr.      Milford, OH  45150
Phone (513) 831-5042      Technical Support Phone: (513) 248-1714

Internet:  http://www.ctcusa.com      E-Mail:  support@ctcusa.com

To convert an unsigned integer to a signed integer, use the following formula in the numeric entry tool input address reference field:

ADR=?+((?>0)*65536))