Note:	Enabling_nbios_P9dos

Product:	P9 DOS/Interact Powerstation

Date:	11-7-00

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

Enabling NetBios on a DOS/Interact Only P9 Workstation

# You will need to edit 3 files on the unit(s).  The Autoexec.bat, Net.bat and the Net.cfg files

## The Autoexec.bat:

--Locate the following lines in the Autoexec.bat—

REM ********************************************************************

REM Load NETWORK drivers -- NOVELL and/or TCPIP stack.

REM Remove REM on the CALL statement to load NOVELL network batch file.

REM If used, this must be called BEFORE loading the TCPIP stack.

REM ********************************************************************

CD \NET

REM CALL C:\NET\NET.BAT

LH C:\NET\TCPIP

STEP #1

1a:  Remove the REM statement from in front of:      CALL C:\NET\NET.BAT

1b:  ADD a REM statement in front of the line above:   LH C:\NET\TCPIP

### SAVE and EXIT

NOTE:  If you plan to also do TCPIP Ethernet Downloads to your P9 Powerstation, you should not add the REM statement to the line above found in 1b.  You will also have to make configuration changes on the Powerstation’s Net setup for Net-1.  (You will need to change the interface type to ODI)

The Net.bat:

--Locate the following lines in the Net.bat.  This file is located on the P9’s Compact Flash or Harddrive in the C:\NET directory.--

REM ********************************************************************

REM Uncomment the appropriate driver:

REM   NE2000   - 10BaseT ethernet

REM   E100BODI - 100BaseT ethernet

REM ********************************************************************

LH NE2000

REM #LH PRO100\E100BODI

# STEP #1

1a:  Add the REM statement in front of LH NE2000

1b.  Remove the REM # statement from the line REM # LH Pro100\E100BODI

SAVE and EXIT

#### The Net.cfg:

--Locate the following lines in the Net.cfg.  This file is located on the P9’s Compact Flash or Harddrive in the C:\Net Directory.--

# Uncomment the appropriate "Link driver" statement:

#   NE2000   - 10BaseT ethernet

#   E100BODI - 100BaseT ethernet

Link driver NE2000

#Link driver E100BODI

Frame Ethernet_802.3

Frame Ethernet_II

Frame Ethernet_802.2

Frame Ethernet_SNAP

Protocol IPX 0 Ethernet_802.3

#INT and PORT parameters not needed for E100BODI driver

INT  10

PORT 280

# STEP#1

Note:  the # signs are used in place of the REM statements, however, they do the same thing. (Make the line a simple comment)

1a:  Add the # sign in front of the line:   Link driver NE2000

1b:  Remove the # sign before the line: #Link driver E100BODI

SAVE and EXIT

##### Reboot you Powerstation

##### Your unit should now be enabled for NETBIOS communication