Note:	Control Logix Tags

Product:	ABEN driver

Date:	2/7/2002

Application Note

While precautions have been taken in the preparation of this note, CTC and the author assume no responsibility for errors or omissions.  Neither is any liability assumed for damages resulting from the use of the information contained herein.

# ControlLogix addressing format using the Allen Bradley Ethernet Driver

- The Allen-Bradley Ethernet driver (ABEN) allows you to address tags in the ControlLogix 5550 controller using the following format:

Driver_Name \ Node_Number  $  [ProgName] Tag_Name [x,y,z].Bit:Data_Type_Specifier

- Following are explanations of the terms used in the address format. [terms in brackets] are optional

- Driver_Name defaults to ABEN. You can change the driver name through a selection on the Interact Application Manager main menu.

- \ is the delimiter that separates the driver name from the PLC station number.

- Node_Number matches the Clogix setting in the Node List tab

- $ is the delimiter that separates the station number from the address reference.

- ProgName is the name of the program that defines a variable's scope. It specifies where the tag was defined in RSLogix 5000. Consider the following two tags: ABEN\1$_x3bool[12]:BOOL and ABEN\1$mainprogram:B2:BOOL. The ProgName is not defined for the first tag since its scope is global. The tag _x3bool is defined under Controller Tags. The second tag however, is defined within the scope of the program mainprogram and therefore uses the ProgName field.

- : is the delimiter used when the ProgName is specified, separating the program name from the tag reference

- Tag_Name is defined using IEC-1131-3 tag name conventions. The tag name can be either a base tag or a structure of data elements. _x3bool is a structure, while B2 is a base tag.

- [x,y,z] are the optional array index specifiers used to address data in one-, two-, or three-dimensional arrays. Use only one dimension [x] with structured data types.

- . is the delimiter that separates items in the address reference.

- B is the optional bit or character length specifier. Bit specifiers are for SINT (0-7), INT (0-15), and DINT (0-32) character types. The character specifier is for STRING (1-80) data types. This parameter does not apply to BOOL data types.

- T is the data type specifier used to identify the tag data type. Valid options are BOOL, SINT, INT, DINT, REAL, and STRING.It is not required when addressing Product Defined Structures.

3. String Data Types: In a ControlLogix system, ASCII string data is accessed as part of a user-defined data type. The data type is a single-dimension array of DINT data elements. Since each element stores four ASCII characters, the length of the array should be one-fourth of the maximum length needed to store the desired ASCII text. Allen-Bradley recommends limiting ASCII string lengths for the ControlLogix controller to 80 characters or less. Therefore the DINT length should be 20 elements.

Consider the following two Interact tags:

They are defined in RSLogix 5000 as follows

ST10 uses the ST data type defined under the User-Defined section. ST11 is a data type defined as part of the program tags. Both are of type DINT[20] and both must be addressed in Interact with the :STRING at the end.